## Slide 1: Lecture 3
The Boot Process

## Slide 2: Learning Objectives
Understand the boot sequence
First baby step to being “DevOps”

## Slide 3: The Agents in the (Linux) Booting Process
Reset
Reset Vector
BIOS
Master Boot Record
GRUB
(Grand Unified Bootloader)
Kernel
Init
/sbin/init
Runlevel
/etc/rc.d/rc*.d
executes
executes
executes
executes
loads and
executes
fetches
jumps
to

## Slide 4: What happens with the x86 processor boot?
Power sequencing: hardware ensures various power sources are stable at their required voltages
A variety of hardware subsystems starts self-checks and initialization
Processor core’s PC will be set to the reset vector

## Slide 5: Reset vector
The default value of the PC immediately after reset
  After critical power and hardware checks
Hence it is the first instruction fetched
The chipset (the chips supporting the processor) must map this into the BIOS
First instruction is a long jump into the real entry of the BIOS code

## Slide 6: Reset vector
8086 - physical address 0xFFFF0 (16 bytes below 1 MB). CS = 0xFFFF, IP = 0x0000
80286 - physical address 0x000FFFF0 (16 bytes below 1 MB). CS = 0xF000, IP = 0xFFF0
80386 and later x86 processors – 0xFFFFFFF0 (16 bytes below 4 GB). CS selector =0xF000, CS base = 0xFFFF0000, IP = 0xFFF0h

## Slide 7: What about multiprocessor systems?
During the early reset stage, and at the end of the processors internal self-check, a hardware protocol is used to determine the bootstrap processor (BSP)
  The protocol differs from processor generation and implementation but basically involve a competition for some kind of semaphore
  One and only one of the cores will be the bootstrap processor
Only the BSP executes the boot sequence

## Slide 8: BIOS
“Basic Input/Output System”
A firmware for hardware initialization and booting that resides in non-volatile memory
  Updating by “flashing” the EEPROM
As of 2014, new PCs are shipped with its successor Universal Extensible Firmware Interface (UEFI)

## Slide 9: BIOS Implementations
Source: Wikipedia

## Slide 10: Power-on Self-test (POST)
Executed very early in the BIOS code
Typical steps:
  verify CPU registers
  verify the integrity of the BIOS code itself
  verify some basic components like DMA, timer, interrupt controller
  find, size, and verify system main memory
  initialize BIOS
  pass control to other specialized extension BIOSes (if installed)
  identify, organize, and select which devices are available for booting, organize, and select which devices are available for booting

## Slide 11: Real mode
In real mode, memory is limited to 1MB
Upon power up, top 12 address lines asserted high, forcing address to 0xFFFxxxxx
If no mode transition after first long jump, enters real mode
  Memory limited to 1MB

## Slide 12: X86 mode changes

## Slide 13: DOS memory management (Real mode)
Upper memory area (UMA) refers to the address space between 640 KB and 1024 KB (0xA0000–0xFFFFF).
Three 128 KB regions were defined in this area.
  The 128 KB region between 0xA0000 and 0xBFFFF was reserved for video adapter screen memory.
  The 32 KiB region between 0xC0000 and 0xC7FFF was reserved for video adapter Video BIOS memory.
  The 160 KiB region between 0xC8000 and 0xEFFFF was reserved for device Option ROMs, and special RAM usually shared with physical devices
- Wikipedia

## Slide 14: Digression – a pain from the past: A20
The original 8086 supports 1MB of memory.
But with real-address mode segmentation, one can have a segment register with value 0xFFFF and an offset of 0xFFFF
  Written as ‘FFFF:FFFF’
FFFF:FFFF gives an effective address of 0x10FFEF (which is 21 bits!)
  On 8086, it is ‘wrapped around’ to yield the address 0x0FFEF
80286 onwards gives an additional A20 (the 21st) address line
  AND THE OPTION TO TURN IT ON OR OFF
  VIA PROGRAMMING THE KEYBOARD!
https://wiki.osdev.org/A20_Line

## Slide 15: The “Unreal” Mode
A small digression

## Slide 16: “Unreal” Mode
Real mode 1MB memory constraint is too restrictive
A clever exploit of the Intel ISA allows for real mode addressing to go beyond 1MB
The main hurdle is the limit of using only 20 bit addresses
To get into “unreal” mode, need to do a real mode to protected mode switch and then back to real mode

## Slide 17: Segment Descriptor Cache Register
Used to speed up protected mode segment addressing
Protected mode addressing
If no change
then no change in these either
Cache it!

## Slide 18: Segment Descriptor Cache
Format varies but…
after 80386 all segment limits
are 32 bits

## Slide 19: Using “Unreal” Mode - 1
Start in real mode. Do a switch to protected mode.
Set up the descriptors, selectors and GDT. Most important, set limit to 4GB. Make sure privilege level set appropriately.
Segment Descriptor
Segment Selector

## Slide 20: Using “Unreal” Mode - 2
Switch back to real mode. Cache limit remains and takes precedence.
Use the “operand size prefix” (0x66) in instructions to enable the use of longer than 16 bit offset registers.
In (normal) real mode, address = seg * 16 + offset. If total sum exceeds 1MB, instruction fault.
In “unreal” mode, offset can now be full 32 bits (using the operand size prefix for some instructions) so while still address = seg * 16 + offset, since offset can be 32 bits, address can be 32 bits.

## Slide 21: “Unreal” mode - caveat
Real mode interrupt assumes 16 bits IP. Code segment above 64KB needs special attention.
Unreal mode can be used by boot routines or for writing/supporting backward compatible applications
  E.g. DOSBox
Requires special compiler support to generate the prefix

## Slide 22: Back to our boot story…

## Slide 23: BIOS software setup
At least must load an Interrupt Descriptor Table (IDT), a Global Descriptor Table (GDT), a Task-State Segment (TSS), and, optionally, a Local Descriptor Table (LDT).
Must also initialize some critical control registers and the memory type range registers (MTRR)
Once these set up, ready to boot the OS.
  Note: still in real mode!

## Slide 24: Memory Type Range Registers (MTRR)
MTRRs provide a mechanism for associating the memory types with physical-address ranges in system memory
Allows up to 96 memory ranges to be defined in physical memory

## Slide 25: “Pre-memory”
Memory itself is a hardware resource and the memory controller itself must be set up
Prior to the set up (including testing), no DRAM is available
  Thus far we are in read-only ROM BIOS and register land
In particular, no stack – hence no procedure call
To circumvent this, one way is to use the cache as memory
  “No evict mode” – no eviction on miss
  By setting the appropriate MTRR
  Must “undo” after memory is available

## Slide 26: “Post-memory”
With memory up and available, BIOS is ready to load in OS
Initialize secondary storage devices, scan boot sequence to find the master boot record (MBR) and verify its integrity
If all goes well, load the bootstrap loader – the code section of the MBR
  For Intel, physical address 0x7C00
Does a jump to the bootstrap loader

## Slide 27: Intel Memory Map at Boot up

## Slide 28: Master Boot Record
Master Boot Record
Partition Table Entry

## Slide 29: Disk partitions
Disk partitioning is a way of organizing a physical disk.
A physical disk can contain multiple partitions, each a logical disk
Advantages:
  Separate uses: OS, swap disk, user files
  Some protection from misuse and corruption
  “Short stroking”: reduce seek time as files are more localized
Disadvantages:
  Increases fragmentation
  Can restrict use

## Slide 30: And in comes GRUB
For Linux, MBR is the first stage of GRUB, boot.img (GRUB stage 1)
  See http://www.funtoo.org/Boot_image for annotated GRUB MBR
Up to now, everything is in real mode (or possibly unreal mode)
Boot.img locates and reads in diskboot.img and jumps to it (at location 0x2000)
Diskboot.img loads in the rest of GRUB (GRUB Stage 1.5)
  Including drivers for handling (key) file systems
Control is transferred to grub_main() finally

## Slide 31: The Linux/x86 Boot Protocol
https://www.kernel.org/doc/Documentation/x86/boot.txt
Dictates the memory layout, structures and initial values expected by the Linux kernel before and during the boot process

## Slide 32: grub_main() – GRUB Stage 2
Initializes the console
Gets the base address for modules
Sets the root device
Loads/parses the grub configuration file
Loads modules
Fill in the Linux kernel header
The Linux Kernel Header
arch/x86/boot/header.S

## Slide 33: Memory map after kernel load
GRUB loads in both the kernel and RAMdisk. It will exceed the 1MB boundary. So it will transit to protected mode then load.

## Slide 34: GRUB notation
hd stands for hard disk; alternatively, fd stands for floppy disk, cd stands for CD-ROM etc.
The first number refers to the physical hard drive number, starting from 0.
The second number refers to the partition number of the selected hard drive; again, starting from 0.

## Slide 35: GRUB Configuration

## Slide 36: The Linux kernel
vmlinux - a statically linked executable file that contains the entire kernel
vmlinuz – compressed vmlinux
zImage – old kernel below 512KB that is loaded into low memory
bzImage – larger kernel loaded at above 1MB
(These days use vmlinuz directly.)

## Slide 37: initrd
Zen koan: “Before you were born, what was your face?”
Before the OS gets booted, there is no drivers or file system, hence no files
But the boot process requires an environment to work in
Answer: a pre-laid out minimum file system that is so small that it can fit in RAM
  Recall: BIOS brought DRAM on board, albeit in real mode

## Slide 38: initrd
“Initial RAMdisk”: a temporary root file system in memory
  Minimal set of directories and executables to support 2nd stage booting

## Slide 39: initrd vs initramfs
Initrd:
  A full file system image (may be compressed)
  Driver for that file system (ext2, cramfs) must be compiled statically into the kernel
  Can use pivot_root command to change it later
Initramfs:
  A cpio file archive (like tar)
  Unpacked into a file system of OS’s choice (usually tmpfs)
  No need for special drivers compiled into kernel

## Slide 40: Kernel boots
GRUB finally transfers control to _start in arch/x86/boot/header.S
Still in real mode!
  Even though GRUB has loaded kernel and initrd into the higher addresses
More initializations
  Make sure that all segment register values are equal
  Set up a correct stack, if needed
  Set up bss
Jump to the C code in main.c

## Slide 41: arch/x86/boot/main.c
Enters protected mode!

## Slide 42: Switching to Protected Mode
arch/x86/boot/pm.c
arch/x86/boot/pmjump.S

## Slide 43: Decompressing the kernel
Depending on whether the kernel is 32 bits or 64 bits, one of the following will be (eventually) called (in arch/x86/boot/compressed/head_{32|64}.S):
  startup_32
  startup_64
Build page tables
  Linux uses 4-level paging
Decompress kernel via __decompress()

## Slide 44: We are in!
After kernel decompression, control is transferred to startup_{32|64} of arch/x86/kernel/head_{32|64}.S
  Note that this is a different routine from the ones that triggered decompression
More initialization
Eventually start_kernel() of init/main.c is called

## Slide 45: initrd kicks in
Kernel mounts initrd as root, i.e., “/”
After initrd is mounted successfully, the function “run_init_process()” of init/main.c is called. This will execve the first user level process – init.
  /sbin/init
  /etc/init
  /bin/init
  /bin/sh

## Slide 46: The init process
Distro dependent
Switches from initrd over to a disk root file system
  Need to first load all the necessary drivers
init is the parent of all processes
Bulk of the boot messages originate from this point on
Culminates in the user selecting a bootlevel

## Slide 47: systemd

## Slide 48: systemd
Alternative to init
Starts processes in parallel
Supports interactive booting
Simpler API
x86 only (for now)
Still controversial

## Slide 49
Features | init | systemd
Quota Management | No | Yes
Automatic Service Dependency Handling | No | Yes
Kills users Process at logout | No | Yes
Swap Management | No | Yes
SELinux integration | No | Yes
Support for Encrypted HDD | No | Yes
Static kernel module loading | No | Yes
GUI | No | Yes
List all the child processes | No | Yes
Interactive booting | No | Yes
Portable to non x86 | Yes | No
Adopted on | Several Distro | Several Distro
Parallel service startup | No | Yes
Resource limit per service | No | Yes
Easy extensible startup script | Yes | No
Separate Code and Configuration File | Yes | No
Automatic dependency calculation | No | Yes
Size | 560 KB | N/A
Number of Files | 75 files | 900 files + glib + DBus
Lines of code – LOC | ≈15,000 | ≈224,000
Source: https://www.tecmint.com/systemd-replaces-init-in-linux/

## Slide 50: Configuration directories
/etc/systemd – Local configuration information
/run/systemd – Temporary files (testing, etc.)
/usr/lib/systemd – Vendors

## Slide 51: Units
In systemd, everything is a unit
Units have
  A Type
  A State
  May have a Status
A unit has a (usually unique) base‐name
Base‐name + Type = complete unit name

## Slide 52: Unit types

## Slide 53: Dependencies and Ordering
In systemd, dependencies and ordering determines when to start and stop units
Dependencies:
  “Wants” (soft)
  “Requires” (hard)
Ordering:
  “After”
  “Before”

## Slide 54: The Daemons
systemd ‐ The main systemd process. This is the replacement for “/etc/init”.
journald ‐ Event logging.
networkd ‐ Manages network configuration.
logind ‐ Manages user logins.
udevd ‐ Manages devices.

## Slide 55: Initialization
When running as “init” (PID = 1), the following configuration files are read and acted on accordingly:
  /etc/systemd/system.conf
  /etc/systemd/system.conf.d/*.conf
  /run/systemd/system.conf.d/*.conf
  /usr/lib/systemd/system.conf.d/*.conf

## Slide 56: Initialization
When running as a user processor (PID ≠ 1), the following configuration files are used:
  /etc/systemd/user.conf
  /etc/systemd/user.conf.d/*.conf
  /run/systemd/user.conf.d/*.conf
  /usr/lib/systemd/user.conf.d/*.conf

## Slide 57: Unit files
Each unit has a file in one or more of the following directories:
  /etc/systemd/system
  /usr/lib/systemd/system
Some units have “drop in” files in:
  /etc/systemd/system/<unit>.d/*.conf
  /run/systemd/system/<unit>.d/*.conf
  /usr/lib/systemd/system/<unit>.d/*.conf
See: man systemd.unit

## Slide 58: Using systemd
Management tools (see their man pages):
  systemctl
  journalctl
  systemd-cgls
See: https://www.tecmint.com/systemd-replaces-init-in-linux/
See: http://0pointer.de/blog/projects/systemd-for-admins-1.html

## Slide 59: UEFI

## Slide 60: Successors to BIOS
OpenBIOS: https://openbios.info/Welcome_to_OpenBIOS
Libreboot: https://libreboot.org/
Open Firmware: https://github.com/openbios
Coreboot: https://www.coreboot.org/Welcome_to_coreboot
The main stream one: UEFI

## Slide 61: Unified Extensible Firmware Interface (UEFI)
Successor of traditional BIOS
  Legacy support usually provided in implementations
Able to boot from large disks (over 2TB)
CPU independence
Modular
Uses GUID Partition Tables

## Slide 62: LBA vs CHS
Traditionally, disks are addressed using cylinder/head/sector (CHS) tuples
  Dependent on the physical device
Logical Block Addressing (LBA) introduced in the SCSI standard as an abstraction
Current standard is to use 48-bit LBA
  Access to up to 128 PiB (pebibyte = 10245 bytes)

## Slide 63: LBA  CHS
LBA = (C  HPC + H)  SPT + (S - 1)
C, H and S are the cylinder number, the head number, and the sector number
LBA is the logical block address
HPC is the maximum number of heads per cylinder (reported by disk drive)
SPT is the maximum number of sectors per track (reported by disk drive)
C = LBA  (HPC  SPT)
H = (LBA  SPT) mod HPC
S = (LBA mod SPT) + 1

## Slide 64: GUID Partition Table (GPT) format
A new partition structure for UEFI
  Traditional MBR uses 32 bits to store LBA and worse, partitions of up to 2 TiB size
Now supported by all OSes
For backward compatibility, LBA 0 is basically the same as MBR
  Protective MBR – can only boot via EFI
  Hybrid MBR – contains modified bootloader that knows how to handle GPT in BIOS

## Slide 65: Primary GPT Header

## Slide 66: GUID Partition Entry Format

## Slide 67: Global Unique Identifier (GUID)
Partition Type GUID

## Slide 68: UEFI Boot Process

## Slide 69: UEFI Boot Process
SEC
  Target of reset vector
  Verify integrity of the PEI code
  Set up Cache-as-RAM
  Runs the PEI
PEI
  Initializes hardware
  Loads and execute DXE

## Slide 70: DXE (Driver Execution Environment)
Almost a mini-OS (complex)
  When it is up, there is a file system with various bootloader executables
Goal: setup all the necessary drivers so that the actual OS’s bootloader has most of what it needs to work with
  Architectural abstraction
Finds the EFI_SYSTEM_PARTITION, sets up and mount FAT32 file system
Depending on user preferences, execute the boot loader
  For Linux, usually GRUB 2

## Slide 71: UEFI and SMM

## Slide 72: BIOS vs UEFI boot
UEFI does not run the MBR bootstrap loader
  No 446 byte limit
UEFI loads a FAT32 file system driver and sets up a FAT32 root file system

## Slide 73: UEFI Secure Boot
The danger: the BIOS will boot any software including malware
  Bootkits: kernel mode rootkits (malicious software) that infect startup code
Solution: make sure only boot with certified boot code
  Use standard digital signatures of cryptographic keys

## Slide 74: Basic idea
UEFI comes with a set of keys burnt into ROM
Use keys to authenticate software to be loaded
  Using public key cryptography
Initially, only for Windows (coz UEFI founded by Microsoft and Intel)
  Linux later let in by via “shim”
Windows 11 will require both secure boot as well as TPM 2.0 (Trusted Platform Module – a hardware security chip)

## Slide 75: End