## Slide 1: Lecture 6
Interrupts

## Slide 2: The Nuts and Bolts of Responding to Events
Handling interrupts require both hardware and software cooperation
Hardware Portion
  How x86 handles hardware interrupts
Software Portion
  How a kernel handles interrupts

## Slide 3: The General Computing Environment
Central
Processing
Unit
Main
Memory
I/O
device
I/O
device
I/O
device
I/O
device
system bus

## Slide 4: Why interrupts?
I/O an integral part of any computing system
  Disk drives, keyboard or other human interface, etc.
Apps and users expect responsiveness
The unexpected can arise
  Errors, faults, exceptions

## Slide 5: Instruction Processing Cycle
Fetch instruction at IP
Advance IP to next instruction
Decode the fetched instruction
Execute the decoded instruction
Interrupt?
no
Save context
Get INTR ID
Lookup ISR
Execute ISR
yes
IRET

## Slide 6: What is an interrupt?
A forced change in the flow of control
Hardware performs simple context switching
Kernel entered at a specific predetermined point
Normal execution resumes with a special “iret” instruction that also restores the context
Many different types for different purposes

## Slide 7: Types of Interrupts
Asynchronous
  Source is external such as I/O device
  Not related to instruction currently being executed
Synchronous (also called exceptions)
  Processor-detected exceptions:
    Faults — offending instruction is retried (eg. page faults)
    Traps — instruction is not retried
    Aborts — major error (hardware failure)
  Programmed exceptions:
    Requests for kernel intervention (eg. syscalls)

## Slide 8: Faults
Normal execution cannot continue
Examples:
  Writing to a memory segment marked ‘read-only’
  Reading from an unavailable memory segment (on disk)
  Executing a ‘privileged’ instruction
The causes of ‘faults’ can often be ‘fixed’
If the issue can be resolved, then the CPU can just restart its execution-cycle

## Slide 9: Related: instruction replay
Modern processors have deep pipeline and superscalar execution
Corollary: aggressive instruction issue means that an instruction may be issued before it is known to be safe to do so
  Problem: deep into an instruction’s execution, dependency or exception arise
Since Pentium 4, Intel has implemented a hardware replay queue
  Faulting instructions will be placed in a queue to be replayed

## Slide 10: Traps
Example: A CPU might have been programmed to automatically switch control to a ‘debugger’ program at specific program point
  INT 3 (opcode 0xCC) used by debuggers on x86
This is known as a ‘trap’
  Coz it is deliberately set

## Slide 11: Error Exceptions
Most error exceptions are translate directly into signals
  Divide by zero
  Privileged instruction
  Illegal memory referencing, etc.
The kernel’s job is fairly simple: send the appropriate signal to the current process
  force_sig(sig_number, current);
Most of the time, the process by default gets killed
  That’s not the concern of the exception handler
One important exception: page fault
An exception can (infrequently) happen in the kernel
  die(); // kernel oops

## Slide 12: Interrupt: The Hardware Story

## Slide 13: In the good old days…
x86
CPU
Master
PIC
(8259)
Slave
PIC
(8259)
INTR
Programmable Interval-Timer
Keyboard Controller
Real-Time Clock
Legacy PC Design
SCSI Disk
Ethernet
IRQs
Interrupt Request (IRQ)

## Slide 14: Intel 8259 Programmable Interrupt Controller
Expands on the original interrupt capability of the 8085 processor
Can accept 8 interrupt requests, allowing them one by one to the processor INTR pin
Programmable priorities of interrupts
Can be cascaded to allow up to 64 interrupts

## Slide 15: How it worked - 1
First, it has to be initialized
When ready, it receives interrupt through IR0 to IR7
Checks if an interrupt is masked or not, and what is its priority
If all ok (previous interrupt completed, current interrupt highest priority and not masked), send INT signal to INTR pin of 8085
In response, processor sends three INTA signal

## Slide 16: How it worked - 2
Processor sends first INTA signal
8259 responds with x86 CALL opcode
Processor sends second INTA signal
8259 responds with low byte of call address
Processor sends third INTA signal
8259 responds with high byte of call address
Processor saves current PC on stack, executed CALL instruction using the 16-bit address (the interrupt servicing routine) the 8259 sent

## Slide 17: Advanced Programmable Interrupt Controller (APIC)
8259 cannot handle multiprocessor system
  With more than one CPUs, send interrupt to who?
  How to implement inter-processor interrupt (IPI)?
PIC updated with the APIC – actually a system
In APIC, each CPU consists of a “core” and a “local APIC” (LAPIC)
  Contains a Local Vector Table
In addition, there is an separate I/O APIC
  Part of the chipset
  If system has multi I/O subsystem, then multiple I/O APIC

## Slide 18: APIC, IO-APIC, LAPIC
Advanced PIC (APIC) for multiprocessor systems
  Used in all modern systems
  Interrupts “routed” to CPU over system bus
  Supports inter-processor interrupt (IPI)
Local APIC (LAPIC) versus “frontend” IO-APIC
  Devices connect to front-end IO-APIC (cascading)
  IO-APIC communicates (over bus) with Local APIC
Interrupt routing
  Allows broadcast or selective routing of interrupts
  Ability to distribute interrupt handling load
  Routes to lowest priority process
    Special register: Task Priority Register (TPR)
  Arbitrates (round-robin) if equal priority

## Slide 19: APIC system

## Slide 20: Local APIC

## Slide 21: Interrupts to Local APIC
Locally connected I/O devices — An I/O device that is connected directly to the processor’s local interrupt pins (LINT0 and LINT1
Externally connected I/O devices — Connected to the interrupt input pins of an I/O APIC
Inter-processor interrupts (IPIs) — For software self-interrupts, interrupt forwarding, or preemptive scheduling.
APIC timer generated interrupts
Performance monitoring counter interrupts
Thermal Sensor interrupts — When the internal thermal sensor has been tripped
APIC internal error interrupts

## Slide 22: Local Vector Table
The processor’s LINT0 and LINT1 pins, the APIC timer, the performance-monitoring counters, the thermal sensor, and the internal APIC error detector are referred to as local interrupt sources
A (programmable) local vector table is looked up to translate these to system-wide interrupt vectors

## Slide 23: I/O APIC
Intel 82093AA (IOAPIC)
PCI chip

## Slide 24: I/O APIC
Each IRQ associated with a 64 bit register

## Slide 25: Intel Reserved Interrupts
Intel Reserved

## Slide 26: Assigning IRQs to Devices
IRQ assignment is hardware-dependent
  Sometimes it’s hardwired, sometimes it’s set physically, sometimes it’s programmable
PCI bus usually assigns IRQs at boot
Some IRQs are fixed by the architecture
  IRQ0: Interval timer
  IRQ2: Cascade pin for 8259A
Linux device drivers request IRQs when the device is opened
Two devices that aren’t used at the same time can share an IRQ, even if the hardware doesn’t support simultaneous sharing

## Slide 27: Assigning Vectors to IRQs
The interrupt vector is an index (0-255) into the interrupt descriptor table
Vectors usually IRQ# + 32
  Below 32 reserved for non-maskable interrupt and exceptions
  Maskable interrupts can be assigned as needed
  Vector 128 used for Linux syscall
  Vectors 251-255 used for IPI

## Slide 28: How x86 handles interrupts

## Slide 29: Basic flow
The Interrupt Descriptor Table Register (IDTR) points to a table (IDT) consisting of either:
  Task-gate descriptor
  Interrupt-gate descriptor
    Disables further interrupts
  Trap-gate descriptor
    Further interrupts still allowed
On an interrupt, the vector is used to look up the table and the corresponding actions are taken

## Slide 30: (32 bit) Gate Descriptors
Privilege level
of handler

## Slide 31: Interrupt Procedure Calls
If the handler procedure is going to be executed at a numerically lower privilege level (i.e., higher privilege), a stack switch occurs. The stack specified in the current process’ TSS is used.
Else, use current stack.
You see why we need a faster way to do syscall rather than through interrupts?

## Slide 32: A digression: Task State Segment
Originally meant for hardware task switching in 32-bit
  Never used by Linux for process switching
Still there in 64 bit but in 64 bit hardware task switching is not supported
Basically, a state context with the contents of all registers
Most important use: supply an alternative stack (kernel stack) for calling more privileged procedures
  Only use of it in Linux
  Pointed to by the privileged tr register
IDT can contain task gates and in 32-bit system will trigger a hardware task switch

## Slide 33: Task State Segment
Ring 0 stack
Ring 1 stack
Ring 2 stack
Intended by Intel to be used for interrupt stacks. But Linux only use it for a few severe exceptions like double-fault.
Linux uses one TSS for each CPU
If non-zero…
If zero…

## Slide 34: Interrupt Stack Table
ESTACK_DF
  INT8 - Double Fault Exception
  Invoked when an exception occurs while handling another exception
ESTACK_NMI
  INT2 - Non-maskable interrupt
ESTACK_DB
  Hardware debug interrupts (INT1) and for software debug interrupts (INT3)
ESTACK_MCE
  INT18 – Machine Check Exception
Each stack is of size 4K (1 page)

## Slide 35: Stack Switching
In 32 bit, rely on hardware task switching to switch stack
In 64 bit, done in entry_SYSCALL_64 of arch/x86/entry/entry_64.S

## Slide 36: Linux and IDT
BIOS will initialize and use the IDT
When Linux boots, it will overwrite introduce a new table idt_table
In arch/x86/kernel/traps.c:trap_init() meaningful values will be written in
Later on, drivers will request for IRQ from kernel

## Slide 37: How Linux initialize the IDT
All Linux interrupt handlers are activated via interrupt gates, and all restricted to kernel mode; no user mode access
  Linux calls these “interrupt gates”
Interrupt 4 (overflow), 5 (bounds check), and 128 (int 0x80) activates interrupt gates that are at Ring 3 (user mode)
  Linux calls these “system gates”
Interrupt 3 (breakpoint) is implemented via an interrupt gate at user mode privilege
  Linux calls this “system interrupt gate”
Most Linux trap handlers are activated via trap gates, all restricted to kernel mode
  Linux calls these “trap gates”
The sole use of a task gate in Linux is for the “double fault” exception. It is in Ring 0.

## Slide 38: Multiple IDTs
Immediately after kernel boots:
  early_idts[] in arch/x86/kernel/idt.c:57
Pre-IST stack version:
  def_idts[] in arch/x86/kernel/idt.c:76
Post-IST stack version:
  ist_idts[] in arch/x86/kernel/idt.c:228

## Slide 39: Setting up interrupt handling
There are a number of varieties of IDT entries and their handlers, and macros are used to generate the “entry stubs”
From interrupt 32 (known by a constant FIRST_EXTERNAL_VECTOR) onwards, the interrupts are handled in the same way, with a small exception.
  If local APIC is turned on, then all interrupts above number 236 are “spurious” and treated as error.
  Otherwise, all handled the same way.
All will use sp0 entry stack

## Slide 40: Workflow
Every IDT vector that does not explicitly point somewhere else gets set to the corresponding value in interrupts
Hardware will interrupt a CPU (according to how it is programmed)
The IRQ will fire off the routine specified in the corresponding IDT entry
  IDT entries generated by assembly and macro voodoo
  Special exceptions have special handlers
  General interrupts eventually make their way to common_interrupt() (used to be called do_IRQ)

## Slide 41: /arch/x86/kernel/irq.c
Generated assembly stub would have switch stack
  From entry sp0 to hardirq_stack
Dispatch from a software table for further processing
  request_threaded_irq() by device driver to install an interrupt service routine (ISR) which is a member of struct irq_desc

## Slide 42: /proc/interrupts
i8042 chip is the keyboard and
mouse controller

## Slide 43: Nested interrupts
A second (or even more) interrupt may come while the one is being serviced
Linux used to support nested interrupts but this was removed to avoid complex solutions to interrupt stack overflows issues
However, it is still possible to have nesting between exceptions and interrupts but the rules are fairly restrictive:
  an exception (e.g. page fault, system call) can not preempt an interrupt; if that occurs it is considered a bug
  an interrupt can preempt an exception
  an interrupt can not preempt another interrupt (it used to be possible)

## Slide 44: Nuts and bolts
On entry to an interrupt handling, check if there was a privilege change
  Done by check CS register
    Constant __USER_CS if in user mode
    Constant __KERNEL_CS if in kernel
If a privilege level change, do the same entry steps as SYSCALL
  swapgs to bring in per CPU data structure
  SWITCH_TO_KERNEL_CR3 to bring in full kernel page tables
  Change stack to per task kernel stack
If no privilege level change, do not do these!

## Slide 45: The OS aspect
The Linux Story

## Slide 46: The overall strategy
Divide interrupt handling into two parts
Top half – immediate handler
  Do the absolute minimal to handle the interrupt and return as quickly as possible
    IRQ disabled → acknowledge IRQ → execute device handler → IRET
    Enables near immediate response to new interrupts
    No clear process context
  Push the bulk of the non-critical processing to Part 2
Bottom half – deferrable functions
  Not time critical work
  IRQ enabled – can be interrupted
  Mechanisms: tasklet, softirq, work queue, kernel thread

## Slide 47: Top half
Do the bare minimum amount of work to safely
  Save registers
  Unmask all other interrupts
Exceptions are handled simply by sending a signal to the process that caused the exception
I/O interrupt has to be handled using the current process

## Slide 48: Limitations of an interrupt service routine
Cannot sleep or call something that might sleep
Cannot refer to current (pointer to the current process)
Cannot do kmalloc(…, GFP_KERNEL) (which can sleep)
  Must use kmalloc(…, GFP_ATOMIC) (which can fail)
Cannot call schedule()
Cannot do a down() semaphore call
  But can do an up()
Cannot transfer data to/from user space

## Slide 49: The Interrupt Stacks
Interrupt service routines mostly written in C – hence need stack
Exceptions use the kernel-level exception stack of the current process
  Kernel stack is the stack in the kernel space of the current process
    One per process whose address is located in the process data structure
  The reason why cannot switch user context or sleep
Interrupts uses a hard IRQ stack
  One per processor, only one page frame in size
SoftIRQ uses soft IRQ stack
  On 32 bit x86, a separate soft IRQ stack
  On 64 bit x86, soft IRQ stack == hard IRQ stack, a.k.a. the “interrupt stack”
The latter two configured in the IDT and TSS at boot time

## Slide 50: Three types of interrupts
I/O interrupts – I/O device requires attention
  Three possible types of actions: critical, non-critical, non-critical deferrable
Timer interrupts
Interprocessor interrupts
See: arch/x86/include/asm/idtentry.h

## Slide 51: I/O interrupts
IRQ are few and hence a precious resource
IRQ sharing
  More than one device may share the same IRQ
  Every service routine registered for the same IRQ must be tried coz you don’t know which is the right one
IRQ allocation
  Device driver requests for IRQ assignment at the last possible moment just before use

## Slide 52: A complication in SMP: lost IRQ
IRQ a comes, CPU x handles
IRQ b comes, CPU y handles
Because of interrupt masking at beginning of process, before, say, CPU x can acknowledge, CPU y masks out all interrupts
CPU x mistakenly thinks IRQ a disabled, returns without processing
IRQ a is “lost” (unprocessed)
Needs additional checking for this case

## Slide 53: Bottom Half – deferrable functions
SoftIRQ – “software” IRQ
Tasklet
Work queue
Kernel thread

## Slide 54: SoftIRQ
In many ways, behaves like a hardware IRQ but done entirely in software
Re-entrant code
  Different processors may execute the same softIRQ handlers at the same time
  Must protect data structures using spinlocks
Can be interrupted
  All hardware interrupts enabled
Data structure: softirq_vec[] – an array of handlers

## Slide 55: SoftIRQ vectors
include/linux/interrupt.h

## Slide 56: SoftIRQ processing
Initialization – done by open_softirq()
Activation – raise_softirq()
Masking
  Needed when a processor wants to change the softIRQ data structure
Execution

## Slide 57: Executing softIRQ
Run at various points by the kernel:
  After system calls
  After exceptions
  After interrupts (top halves/IRQs, including the timer intr)
  When the scheduler runs ksoftirqd
Softirq routines can be executed simultaneously on multiple CPUs:
  Code must be re-entrant
  Code must do its own locking as needed

## Slide 58: ksoftirqd
One daemon per processor
Infinite loop check for and servicing softIRQ on that particular processor

## Slide 59: Tasklets
Implemented on top of softIRQ using HI_SOFTIRQ and TASKLET_SOFTIRQ
Only real difference: HI_SOFTIRQ-based tasklets run prior to the TASKLET_SOFTIRQ tasklets
Invoked either the tasklet_schedule( ) function or the tasklet_hi_schedule( )

## Slide 60: Tasklets vs softIRQ
Tasklets can be statically or dynamically allocated
  SoftIRQ is fixed
Tasklets are not re-entrant
  Tasklets of the same type runs serially in the entire system
  Two tasklets of different types may run concurrently

## Slide 61: Work Queues
SoftIRQ and tasklets run in the interrupt context, work queue functions run in the process context
Work queue functions allowed to sleep
All cannot access user space
Work queues can be created dynamically
Or use the predefined (per CPU) “events” work queue
A worker thread waits for work in the work queue

## Slide 62: Kernel Threads
Always operate in kernel mode
  Again, no user context
2.6.30 introduced the notion of threaded interrupt handlers
  Imported from the realtime tree
  request_threaded_irq()
  Now each bottom half has its own context, unlike work queues
  Idea is to eventually replace tasklets and work queues

## Slide 63: request_threaded_irq()
Supplies a IRQ number, a handler and a threaded function
Spawns a new kernel thread using the threaded function
Handler is the hard IRQ handler
  Determine interrupt cause
  Returns IRQ_HANDLED or IRQ_WAKE_THREAD
If IRQ_WAKE_THREAD, schedule kernel thread created during setup for execution
As part of thread scheduling, threaded function will eventually be executed

## Slide 64: A comparison
 | ISR | SoftIRQ | Tasklet | WorkQueue | KThread
Will disable all interrupts? | Briefly | No | No | No | No
Will disable other instances of self? | Yes | Yes | No | No | No
Higher priority than regular scheduled tasks? | Yes | Yes* | Yes* | No | No
Will be run on same processor as ISR? | N/A | Yes | Yes | Yes | Maybe
More than one run can on same CPU? | No | No | No | Yes | Yes
Same one can run on multiple CPUs? | Yes | Yes | No | Yes | Yes
Full context switch? | No | No | No | Yes | Yes
Can sleep? (Has own kernel stack) | No | No | No | Yes | Yes
Can access user space? | No | No | No | No | No
*Within limits, can be run by ksoftirqd

## Slide 65: Signals

## Slide 66: Unix Signals
A signal is a notification of an event
User application is stopped immediately
A user-supplied signal handler will execute to completion
  This handler is an userspace procedure
User application will resume where it left off
If no handler supplied, default action is taken
  Usually a core dump followed by process termination

## Slide 67: POSIX.1-1990 Signals

## Slide 68: POSIX.1-2001 Signals

## Slide 69: Other signals

## Slide 70: Examples from the keyboard
Ctrl-c  2/SIGINT signal
  Default handler exits process
Ctrl-z  20/SIGTSTP signal
  Default handler suspends process
Ctrl-\  3/SIGQUIT signal
  Default handler exits process

## Slide 71: Sending signals
You can do it at command line using the kill command
  kill -signal pid
    Send a signal of type signal to the process with id pid
    Can specify either signal type name (-SIGINT) or number (-2)
  If no signal type name or number specified, SIGTERM (15) will be sent
    Default SIGTERM handler exits process
Inside a program:
  Use raise() system call to send to self
  Use kill() system call to send to another process

## Slide 72: Example

## Slide 73: Notes and caveats on signal
Use sigprocmask() (and a host of related functions) to check or manipulate the signal mask
  Read the man pages for caveats
If you use the above, watch for race conditions
  Normally, other signals are not raised in a handler as by default blocked

## Slide 74: Kernel handling of user-level signals
Kernel is involved in user-level signal handling because
  Need to interrupt the user process and later resume it
  Signal may arise from exceptions triggered from hardware
  Signals may be sent from one process to another requiring OS checking and intervention
Each process has its own set of signal handlers
Each process can also have a list of pending signals
In multicore systems, possible race conditions
  Need to guard data structures with locks

## Slide 75: Main data structure for signal handling

## Slide 76: The two phases
Signal generation
  Kernel can send signal to user process
  Another process may send signal to a user process
  See functions in kernel/signal.c
  Update the relevant process(es) data structures
    Updates the pending signal list
    If sending another process, and target is sleeping, “kick” that process so that signal will be delivered
    If sending another process, and target is not sleeping, do an interprocessor interrupt
Signal delivery
  Set up invocation of the user level signal handler

## Slide 77: Signal delivery
Before an interrupt routine (in kernel mode) returns to user mode, pending signal is checked
If condition is right, arch_do_signal_or_restart is called which in turns call
arch_do_signal_or_restart is given the current process’ context and signal mask
If no handler, arch_do_signal_or_restart performs the default action; a core dump (usually)
If there is a handler, arch_do_signal_or_restart will call handle_signal()

## Slide 78: handle_signal()
Copies process context from kernel stack into user space stack
Force EIP to point to first instruction of handler
Manipulate user stack such that the handler will return onto the stack which will make a system call to sigreturn()
  Cannot just return simply coz handler may make other system calls – including ones using “int 80h” – an interrupt!
After all these setup, do a true return to user mode

## Slide 79: Linux signal delivery
arch_do_signal_or_restart()
Setup_rt_frame()

## Slide 80: A Quick Word about Windows
User-Mode Driver Framework (UMDF)
UMDF drivers can handle hardware interrupt via the framework
Interrupt objects are created and registered with the framework
Same two-half philosophy:
  OnInterruptIsr – do bare minimum
  OnWorkItem – deferred processing for non-critical part of interrupt processing

## Slide 81: The future is coming

## Slide 82: Linus Torvalds’ Gripe about x86 interrupt handling
IDT itself is horrible, nasty
%rsp not being restored properly by return-to-user mode
delayed debug traps into supervisor mode
several bad exception nesting problems
various atomicity problems with swapgs and stack pointer switching
several different exception stack layouts, and literally hundreds of different entry points for exceptions, interrupts and system calls
    https://www.realworldtech.com/forum/?threadid=200812&curpostid=200822

## Slide 83: AMD’s Supervisor Entry Extensions
https://www.amd.com/system/files/TechDocs/57115.pdf
  Not finalized
Better SYSCALL/SYSRET actions
  Kernel must do certain standard things with potential of non-atomicity
Re-entrant Exceptions
  The same exception occurring during the servicing of that exception

## Slide 84: AMD: Enhanced SYSCALL/SYSRET (ESC)
A new MSR introduced that holds the kernel %rsp
  For SYSCALL/SYSRET
At a Enhanced SYSCALL:
  Enter Ring 0
  Do a SWAPGS
  Swap %rsp with the value in the new MSR
  Create a standard exception frame is on the new stack that contains the next-RIP, CS, RFLAGS, RSP, and SS at the time that SYSCALL was executed
  Load new %rip from the SYSCALL MSR

## Slide 85: AMD: Reentrant Interrupts
A new MSR that contains a bit vector corresponding to x86 exception vectors 0-31. Out of reset, this MSR is set to 0. If bit N is set in this MSR, it means that exception N is in some stage of being handled by software
New Re-entrant Protect (RP) bit in IDT to specify if protection is to be enabled

## Slide 86: AMD: Addition to Interrupt Processing
As before except if RP bit is set, then two additional actions:
  Check the corresponding bit in the new MSR:
    If that bit is 1, generate a double fault. If already in double fault, BSOD!
    If that bit is 0, set that bit and push on as normal
  A 1 byte exception record is written to a new field in the exception frame
    After finishing the current exception processing, then software can decide what to do about this second exception of the same nature

## Slide 87: Intel’s proposal: FRED
Flexible Return and Event Delivery (FRED)
  https://linuxreviews.org/images/c/ca/Intel-346446-flexible-return-and-event-delivery.pdf
Bypass IDT using a new context and a new MSR (IA32_FRED_CONFIG)
Two new return instructions:
  ERETU: returns from Ring 0 to Ring 3
  ERETS: returns from Ring 0 to Ring 0 (no transition)
Automatic SWAPGS operation
Introduces stack levels
  Current Stack Level (CSL): a value from 0-3
  Four new FRED RSP MSRs used to load %rip depending on CSL changes

## Slide 88: FRED Event Delivery
Save up context in temporaries
Determine new %rip
  If oldCPL = 3, %rip = IA32_FRED_CONFIG & ~FFFH
  If oldCPL = 0, %rip = IA32_FRED_CONFIG & ~FFFH + 64
Determine new %rsp from oldCPL
  If already at Ring 0, use same stack (with an option to decrement %rsp)
Push context into new stack
Push additional info about the event onto the new stack (event dependent)
Change CS, SS, and GS if oldCPL = 3
CPL ← 0

## Slide 89: Addition things to note about FRED
SYSCALL/SYSENTER use FRED event delivery as all other interrupts and exceptions
No SYSRET/SYSEXIT
  Use ERETS or ERETU
No word about reentrant exceptions
  Must occur at Ring 0
  Probably left to software to sort out

## Slide 90: Status as of beginning 2022
Whitepaper proposals subject to change
No actual implementation yet
Stay tuned

## Slide 91: End